## Slide 1
Interpreting the world on a
different plane
Robert Bosch Engineering and Business Solutions
BSW – Python Interface Implementation – IOTIC Agents
16th Jan’19
Muthu

## Slide 2: What we have learnt so far.
Setup the environment
Create the user account
Check the connection
Create iotic thing
Show metadata, subscriptions of thing
Adding thing metadata, adding the tags
Follow a feed
Create a feed, add metadata to feed
Share a data to feed
Create control, add metadata to control

## Slide 3: Setup the environment
We installed python 3.7.1- 64-bit in windows platform.
After successful installation we can ensure by running the below command in command prompt. It will show the python version
  python --version
We installed the Iotic Agent by running the below command
  pip install py-IoticAgent
Once it successfully installed we can import the package by running this command
  from IoticAgent import IOT

## Slide 4: Creating the User Account
We can sign up our user account in https://developer.iotic-labs.com/
It will give the free access to iotic Community Space.
Then we can create the agent and we need to generate host, epid, passwd and token.We have to save this file as <agent_name>.ini file
  [agent]
  name = MuthuBosch
  host = broker0.iotic-labs.com:5671
  epid = 5cc0ec0b7aa5bd7bc8f1053f298d7047
  passwd = t7Q7MA0Y3AnJh2FJl9jM7ANtqRr4KTRa
  token = db74c97ef5e71082512771c14f5ff50c369dabae1a681a92ef38d70d76e306db

## Slide 5: Check the Connection
We can check the connection that we are able to connect to iotic space environment by running this command.
To get connected we need the .ini file that we generated from iotic labs.
from __future__ import unicode_literals, print_function # pylint: disable=unused-import
logging.basicConfig(format='%(asctime)s,%(msecs)03d %(levelname)s [%(name)s] {%(threadName)s} %(message)s',
level=logging.CRITICAL)
from IoticAgent import IOT
with IOT.Client(config="Getting_Started.ini") as client: # ADD OWN CONFIG .ini HERE
# do something
print("Connected? ...", client.is_connected())

## Slide 6: Create the thing
We can create the thing by calling the method named “create_thing()”.
We can retrieve the data associated with the thing.
i.e my_thing.lid, my_thing.guid
from IoticAgent import IOT
def connect_thing(client):
print("Connecting my first Thing")
my_thing = client.create_thing('My_First_Thing') # GIVE IT A NAME
print("About my Thing")
print("My Thing object:", my_thing)
print("My Thing local ID (lid):", my_thing.lid)
print("My Thing globally unique ID (guid):", my_thing.guid)
return my_thing
def main():
with IOT.Client(config='Getting_Started.ini') as client: # ADD OWN CONFIG .ini HERE
connect_thing(client)
while True:
try:
print("Main running, press ctrl+c to quit.")
time.sleep(10)
except KeyboardInterrupt:
break

## Slide 7: Show Metadata/Subscriptions of thing
We can get the metadata of thing by calling “get_meta()” method.
We can get the labels, descriptions, location and list of tags by calling below methods.
  get_labels()
  get_descriptions()
  get_location()
  list_tag()
We can the list of subscriptions by calling the below method.
  My_thing.list_connections()
def show_metadata(my_thing):
with my_thing.get_meta() as my_metadata:
my_labels = my_metadata.get_labels()
print(my_labels)
my_descriptions = my_metadata.get_descriptions()
print(my_descriptions)
my_lat, my_lon = my_metadata.get_location()
print("Returned location lat = %f & lon = %f" % (my_lat, my_lon))
print("List of Tags for this Thing:")
tag_list = my_thing.list_tag()
print(tag_list)

## Slide 8: Adding thing metadata and add the tags
We can set the label, description, location to thing metadata by calling below methods.
  Set_label()
  Set_description()
  Set_location()
We can add the tags to a thing by creating the tag and passing the tags.
  My_thing.create_tag(tags)
  My_thing.list_tag()
def add_thing_metadata(my_thing):
with my_thing.get_meta() as my_metadata:
my_metadata.set_label('My First Thing')
my_metadata.set_description('This is a description.')
latitude = 51.5049707142585
longitude = -0.087662711739
my_metadata.set_location(latitude, longitude)
with my_thing.get_meta() as my_metadata:
print("My Thing's metadata object:", my_metadata)
def add_thing_tags(my_thing):
tags = ['HelloWorld', 'tag1', 'tag2']
my_thing.create_tag(tags)
tag_list = my_thing.list_tag()
print(tag_list)

## Slide 9: Follow a Feed
If we want to follow any feed, we need the global point id of that feed.
  Mything.follow(remote_feed_gpid, follow_feed_callback)
def follow_remote_feed(my_thing):
remote_feed_gpid = '335af88a91228a44fb31e9c5e8476861'
remote_feed = my_thing.follow(remote_feed_gpid, follow_feed_callback)
sub_list = my_thing.list_connections()
print("Subscription list: ", sub_list)
def follow_feed_callback(args):
print("Printing data received from followed Feed")
print("This is the Feed Callback with data:", args['data'])

## Slide 10: Create a feed, add metadata to feed
We can create the feed by calling the method “create_feed()”.
We can retrieve the local point id of feed, global point id. We can check whether this is feed or control.
  My_feed.pid
  My_feed.guid
  My_feed.foc
We can add label, descriptions to the feed by calling set_label(), set_description() methods.
def create_feed(my_thing):
my_feed = my_thing.create_feed('My_New_Feed')
print("About my Feed")
print("My Feed object:", my_feed)
print("My Feed local point ID (pid):", my_feed.pid)
print("My Feed global point ID (guid):", my_feed.guid)
print("Check this is a feed or control:", my_feed.foc)
return my_feed
def add_feed_metadata(my_feed):
with my_feed.get_meta() as my_metadata:
my_metadata.set_label('My New Feed')
my_metadata.set_description('"You get nothing from me right now"')
my_labels = my_metadata.get_labels()
my_descriptions = my_metadata.get_descriptions()

## Slide 11: Share a data to Feed
We can share any real time data to the feed by calling below method.
  My_feed.share(data)
def share_data(my_feed):
print("Sharing Values")
current_values = {}
current_values["timestamp"] = time.strftime("%Y-%m-%dT%H:%M:%S", time.localtime())
my_feed.share(current_values)

## Slide 12: Create control, add metadata to control
We can create the control by calling create_control() method.
We can retrieve the parameters associated with control as below.
  My_control.pid
  My_control.lid
  My_control.guid
  My_control.foc
We can set the label and description for control as below.
  My_metadata.set_label()
  My_metadata.set_description().
def create_control(my_thing):
my_control = my_thing.create_control('My_Controllable_Point', ctrl_callback)
print("My Control object:", my_control)
print("My Control local ID (pid):", my_control.pid)
print("My Thing local ID that advertises this Control (lid):", my_control.lid)
print("My Control globally unique ID (guid):", my_control.guid)
print("Check this is a feed or control:", my_control.foc)
return my_control
def add_control_metadata(my_control):
with my_control.get_meta() as my_metadata:
my_metadata.set_label('My Controllable Point')
my_metadata.set_description('"Just prints the data received"')
my_labels = my_metadata.get_labels()
my_descriptions = my_metadata.get_descriptions()

## Slide 13: THANK YOU
MUTHU